## Slide 1: SAP-2
Md. Aashikur Rahman Azim
Lecturer
CSE, BUET

## Slide 2: Introduction
SAP-2 is the next step in the evaluation toward modern computers.
It includes jump instructions.

## Slide 3: Bidirectional Registers
Either enable or load only active .
During load input lines active output line float
During Enable output lines active input line float.
Input and output pins are shorted.
Single set of wires(path) between register and w-bus.

## Slide 4: Bidirectional Registers
LOAD
CLK
Enable
BUS

## Slide 5: Architecture
Encoder
Hexa
In Port 1
In Port 2
PC
MAR
A
ALU
TEMP
B
C
8
8
8
8
8
16
Bus W
Memory
MDR
IR
CON
Out Port 3
Out Port 4
16
8
8
8
8
8
16
8
8
8
8
8
8
Hexa Disp
Flag
8
2
Serial In
Ack
0
7
Ready
Serial Out
Ack
0
7

## Slide 6: Input port
Port 1 and Port 2
Port 1
Hexadecimal keyboard encoder
Sends ready signal to bit 0 of port 2 (indicates the data in port 1 is valid)
Port 2
Serial In

## Slide 7: Program Counter
16 bit address
Thus can count from
PC= 0000 0000 0000 0000
PC= 1111 1111 1111 1111(FFFFH)
LOW CLR’

## Slide 8: MAR and MEMORY
16- bit address to MAR (From 0000H  FFFFH)
MAR OUTPUT to RAM
Memory Capacity(?????)
2K ROM(0000H-07FFH) => Monitor Program
62K RAM(0800H-FFFFH)
ROM
RAM
0000 H
07FF H
0800 H
FFFF H

## Slide 9: Memory Data Register
8-bit Register
Output setup RAM
Receives data from the bus before write operation
Data to the bus after read operation

## Slide 10: Instruction Register
8-bit op code
Can accommodate 256 instruction
Only 42 instruction

## Slide 11: Controller Sequencer
As usual
Generates the control words (microinstructions)
Has more hardware(larger number of instruction)
Control Word is bigger (CON)

## Slide 12: Accumulator
Same as SAP-1

## Slide 13: ALU and Flags
ALU: Includes both arithmetic and logical operation
4 or more control bits for determining the operation to be performed
Flag: Represent the status of the arithmetic and logical operation
Filp flops are used;
    Zero Flag(Z)
    Sign Flag(S)

## Slide 14: Temp, B and C registers
Temporary register (TEMP)
Register B and C are used to move data during program run and accessible to programmers.

## Slide 15: Output Ports
2 output ports(3 and 4)
Port 3 : Drives Hexadecimal display
Port 4: sends ACKNOWLEDGE signals used to hexadecimal encoder. (Handshaking)
Serial Out: Serial Transmission of data.

## Slide 16: Microprocessor Instruction
LDA and STA
Eg:
LDA 2000H
STA 8000H

## Slide 17: MVI
MVI-Move Immediate
MVI A,37H
MVI A,byte
MVI B,byte
MVI c, byte

## Slide 18: Register Instruction
MOV
MOV A,B
MOV A,C
MOV B,A
MOV B,C
MOV C,A
MOV C,B

## Slide 19: Register Instruction
ADD and SUB
Eg ADD B /SUB B
ADD B
ADD C
SUB B
SUB C

## Slide 20: Register Instruction
INR and DCR
INR A/DCR A
INR B/DCR B
INR C/DCR C

## Slide 21: Jump And Call Instruction
JMP
JMP 3000H
JM (Jump if Minus)
JZ(Jump if zero)
JNZ(Jump if not zero)

## Slide 22: Jump And Call Instruction
CALL
Subroutine ????
Call is used to call the subroutine
Ret
Return back from subroutine
Program Counter contents ????
-----stored in the last two location of memory
(FFFEH and FFFFH)

## Slide 23: Logic Instruction
CMA-Complement the accumulator
ANA-And the accumulator with specified register
eg ANA B
ORA- OR the accumulator with specified register
eg ORA B
XRA- XOR the accumulator with specified register
eg XRA B

## Slide 24: Logic Instruction Contd.
ANI: And Immediate
Eg ANI C7H (AND accumulator with immediate data C7H)
ORI: OR immediate
Eg ORI C7H
XRI: XOR immediate
Eg XRI C7H

## Slide 25: Other Instruction
OUT (OUT byte eg: OUT 03H: accumulator to designated port)
HLT
IN (Input : Enter the data from designated input port to accumulator) eg: IN 02H
NOP
RAL(Rotate the accumulator left)
  A=1011 0100 After execution
  A=0110 1001
RAR (Rotate the accumulator right)
  A= 1011 0100
  After execution
  A=0101 1010

## Slide 26: SAP-2 Op codes

## Slide 27: Instruction Affecting Flags

## Slide 28: T-States
Fetch  3 T-States
Execution  Different instruction requires different # of T-States
Ex: ADD B  4
ANI byte  7
CALL  18
JM  10/7

## Slide 29: Summary 1

## Slide 30: Summary 2

## Slide 31: Math-1

## Slide 32: Solution of Math-1

## Slide 33: Math-2

## Slide 34: Solution of Math-2

## Slide 35
Thank you