## Slide 1: SAP-3
Md. Aashikur Rahman Azim
Lecturer
CSE, BUET

## Slide 2: Introduction
SAP-3 is an 8-bit microcomputer that is upward compatible with 8085.
SAP3 includes all SAP2 features.
It includes stack operations.

## Slide 3: SAP2 - Architecture
Encoder
Hexa
In Port 1
In Port 2
PC
MAR
A
ALU
TEMP
B
C
8
8
8
8
8
16
Bus W
Memory
MDR
IR
CON
Out Port 3
Out Port 4
16
8
8
8
8
8
16
8
8
8
8
8
8
Hexa Disp
Flag
8
2
Serial In
Ack
0
7
Ready
Serial Out
Ack
0
7

## Slide 4: Architecture (Like as SAP2)
PC
SP
F
E
D
C
B
A
H
L

## Slide 5: Program Counter
16 bit address
Thus can count from
PC= 0000 0000 0000 0000
PC= 1111 1111 1111 1111(FFFFH)

## Slide 6: Memory Data Register
8-bit Register
Output setup RAM
Receives data from the bus before write operation
Data to the bus after read operation

## Slide 7: Instruction Register
8-bit op code
Can accommodate 256 instruction
Around 246 instructions

## Slide 8: Controller Sequencer
As usual  Like SAP2

## Slide 9: Accumulator
Same as SAP-1

## Slide 10: ALU and Flags
ALU: Includes both arithmetic and logical operation
4 or more control bits for determining the operation to be performed
Flag: Represent the status of the arithmetic and logical operation
8-bit Register Used;
    Zero Flag(Z)
    Sign Flag(S)
    Carry Flag(CY)
    Parity Flag (P)

## Slide 11: Temp
Temporary register (TEMP)  like SAP2

## Slide 12: Microprocessor Instructions

## Slide 13: MOV & MVI
MOV reg1, reg2
reg1 = A, B, C, D, E, H, L
reg2 = A, B, C, D, E, H, L
MVI reg, byte
reg = A, B, C, D, E, H, L

## Slide 14: Carry Flag (CY)

## Slide 15: Carry Flag (CY) Contd.
Add  Carry
Sub  Borrow

## Slide 16: Carry Flag Instructions
STC  SeT Carry (CY =1)
CMC  CompleMent Carry
    CY =

## Slide 17: ADD
ADD reg
reg = A, B, C, D, E, H, L

## Slide 18: ADC
ADC  ADD with Carry (CY).
SUB reg
reg = A, B, C, D, E, H, L
Example: A = 1111 1111 E = 0000 0000 CY =1.
SBB E  1111 1111
+ 0000 0001
-----------------------------------------------
10000 0000
 At the End, CY = 1. A = 0000 0000

## Slide 19: SUB
SUB reg
reg = A, B, C, D, E, H, L

## Slide 20: SBB
SBB  Subtract with borrow (CY).
SUB reg
reg = A, B, C, D, E, H, L
Example: A = 1111 1111 E = 0000 0010 CY =1.
SBB E  1111 1111
- 0000 0011
-----------------------------------------------
1111 1100

## Slide 21: Increment
INC reg
reg = A, B, C, D, E, H, L
INC has no effect on the carry.

## Slide 22: Decrement
DEC reg
reg = A, B, C, D, E, H, L
DEC has no effect on the carry.

## Slide 23: RAL & RAR
RAL  Rotate All Left (a)
RAR  Rotate All Right (b)

## Slide 24: RLC & RRC
RLC  Rotate Left with Carry (a)
RRC  Rotate Right with Carry (b)
Multiplication & Division

## Slide 25: Logic Instructions
ANA reg
ORA reg
XRA reg
reg = A, B, C, D, E, H, L

## Slide 26: Compare Instruction
CMP reg
reg = A, B, C, D, E, H, L
Z flag effected after the operation

## Slide 27: Arithmetic & Logic Immediate
ANI byte
ORI byte
XRI byte
ADI byte  ADD immediate
ACI byte  ADD with carry immediate
SUI byte  SUB immediate
SBI byte  SUB with borrow immediate
CPI byte  Compare Immediate

## Slide 28: Parity Flag (P)
P = 1, if A has EVEN number of ‘1’
P = 0, otherwise

## Slide 29: Jump And Call Instruction
SAP2
JMP address
JM (Jump if Minus)
JZ(Jump if zero)
JNZ(Jump if not zero)
SAP3
JP (Jump if positive)
JC ( Jump id Carry)
JNC ( Jump if not Carry)
JPE (Jump if Even Parity)
JPO (Jump if Odd Parity)

## Slide 30: Extended Register
Register pairs  16 bits
3 pairs (BC, DE and HL)

## Slide 31: Extended Instructions
X  for Extended instruction
LXI B, dble
LXI D, dble
LXI H, dble
Example: LXI B, 90FFH
B = 90H, C = FFH

## Slide 32: Extended Instructions
DAD instruction  Double ADD
DAD B
DAD D
DAD H
Here, default register Pair is HL, works like A for extended ADD.

## Slide 33: Extended Instructions
INX & DCX instruction
INX B, INX D, INX H
DCX B, DCX D, DCX H
No Flags will be effected after these operations.

## Slide 34: Indirect Instructions
The HL register pair points to the memory locations where data is stored, means HL is a data pointer.
LDA address and STA address
HL = address
Use HL pair to access memory location

## Slide 35: Indirect Read
MOV reg, M
reg = A, B, C, D, E, H, L
M = memory address
HL  M

## Slide 36: Indirect Write
MOV M, reg
reg = A, B, C, D, E, H, L
M = memory address
HL  M

## Slide 37: Indirect Immediate Instructions
MVI M, byte
M = memory address
HL  M

## Slide 38: Other Instructions by HL pointer
ADD M
ADC M
SUB M
SBB M
INC M
DEC M
ANA M
ORA M
XRA M
CMP M

## Slide 39: STACK Instructions
Begin Address: 20FFh
End Address: 20E0h
PUSH, POP
Before call we need to store registers & Flags
PUSH B (BC)
PUSH D (DC)
PUSH H (HL)
PUSH PSW

## Slide 40: PUSH operation
When PUSH instruction is executed, the following things happen:
  The SP is decremented to get a new value of SP-1
  The high byte in the specified register pair is stored in M[SP-1]
  The SP is decremented again to get SP-2
  The low byte in the specified register pair is stored in M[SP-2]

## Slide 41: POP Operation
When POP is executed, the following happens:
  REVESE of PUSH !!

## Slide 42: Call & RET Instructions
CALL
Subroutine ????
Call is used to call the subroutine
Ret
Return back from subroutine
Program Counter contents and other values (FLAGS) ????
-----stored in the STACK

## Slide 43: Conditional CALLs
CNZ address
CZ address
CNC address
CC address
CPO address
CPE address
CP address
CM address

## Slide 44: Conditional RETURNs
RNZ
RZ
RNC
RC
RPO
RPE
RP
RM

## Slide 45
Thank you