## Slide 1: Memory Hierarchy and Caches

## Slide 2: Cache Memories in the Datapath
I-Cache miss or D-Cache miss causes pipeline to stall
ALU result
32
0
1
D-Cache
Address
Data_in
Data_out
32
R
D
Rd3
Data
Rd4
32
A
L
U
32
A
B
Rd2
clk
5
Rs
5
Rd
Rt
32
Register File
RA
RB
BusA
BusB
RW
BusW
0
1
Ext
0
2
3
1
0
2
3
1
I-Cache
Address
PC
Instruction
Instruction
Imm16
Interface to L2 Cache or Main Memory
I-Cache miss
D-Cache miss
Instruction Block
Data Block
Block Address
Block Address
Imm
1
0
0
2
1

## Slide 3: Four Basic Questions on Caches
Q1: Where can a block be placed in a cache?
  Block placement
  Direct Mapped, Set Associative, Fully Associative
Q2: How is a block found in a cache?
  Block identification
  Block address, tag, index
Q3: Which block should be replaced on a cache miss?
  Block replacement
  FIFO, Random, LRU
Q4: What happens on a write?
  Write strategy
  Write Back or Write Through cache (with Write Buffer)

## Slide 4: Inside a Cache Memory
Processor
Cache
Memory
Main
Memory
Address
Data
Address
Data
Cache Block (or Cache Line)
  Unit of data transfer between main memory and a cache
  Large block size  Less tag overhead + Burst transfer from DRAM
  Typically, cache block size = 64 bytes in recent caches
Address Tag 0
Address Tag 1
Tag N – 1
Cache Block 0
Cache Block 1
Cache Block N – 1
N Cache Blocks
Tags identify
blocks in
the cache
. . .
. . .

## Slide 5: Block Placement: Direct Mapped
Block: unit of data transfer between cache and memory
Direct Mapped Cache:
  A block can be placed in exactly one location in the cache
000
001
010
011
100
101
110
111
00000
00001
00010
00011
00100
00101
00110
00111
01000
01001
01010
01011
01100
01101
01110
01111
10000
10001
10010
10011
10100
10101
10110
10111
11000
11001
11010
11011
11100
11101
11110
11111
In this example:
Cache index =
least significant 3 bits of Memory address
Cache
Main
Memory

## Slide 6: Direct-Mapped Cache
A memory address is divided into
  Block address: identifies block in memory
  Block offset: to access bytes within a block
A block address is further divided into
  Index: used for direct cache access
  Tag: most-significant bits of block address
  Index = Block Address mod Cache Blocks
Tag must be stored also inside cache
  For block identification
A valid bit is also required to indicate
  Whether a cache block is valid or not
V
Tag
Block Data
=
Hit
Data
Tag
Index
offset
Block Address

## Slide 7: Direct Mapped Cache – cont’d
Cache hit: block is stored inside cache
  Index is used to access cache block
  Address tag is compared against stored tag
  If equal and cache block is valid then hit
  Otherwise: cache miss
If number of cache blocks is 2n
  n bits are used for the cache index
If number of bytes in a block is 2b
  b bits are used for the block offset
If 32 bits are used for an address
  32 – n – b bits are used for the tag
Cache data size = 2n+b bytes
V
Tag
Block Data
=
Hit
Data
Tag
Index
offset
Block Address

## Slide 8: Mapping an Address to a Cache Block
Example
  Consider a direct-mapped cache with 256 blocks
  Block size = 16 bytes
  Compute tag, index, and byte offset of address: 0x01FFF8AC
Solution
  32-bit address is divided into:
    4-bit byte offset field, because block size = 24 = 16 bytes
    8-bit cache index, because there are 28 = 256 blocks in cache
    20-bit tag field
  Byte offset = 0xC = 12 (least significant 4 bits of address)
  Cache index = 0x8A = 138 (next lower 8 bits of address)
  Tag = 0x01FFF (upper 20 bits of address)
Tag
Index
offset
4
8
20
Block Address

## Slide 9: Example on Cache Placement & Misses
Consider a small direct-mapped cache with 32 blocks
  Cache is initially empty, Block size = 16 bytes
  The following memory addresses (in decimal) are referenced:
  1000, 1004, 1008, 2548, 2552, 2556.
  Map addresses to cache blocks and indicate whether hit or miss
Solution:
  1000 = 0x3E8 cache index = 0x1E Miss (first access)
  1004 = 0x3EC cache index = 0x1E Hit
  1008 = 0x3F0 cache index = 0x1F Miss (first access)
  2548 = 0x9F4 cache index = 0x1F Miss (different tag)
  2552 = 0x9F8 cache index = 0x1F Hit
  2556 = 0x9FC cache index = 0x1F Hit
Tag
Index
offset
4
5
23

## Slide 10: Fully Associative Cache
A block can be placed anywhere in cache  no indexing
If m blocks exist then
  m comparators are needed to match tag
  Cache data size = m  2b bytes
m-way associative
Address
Tag
offset
Data
Hit
=
=
=
=
V
Tag
Block Data
V
Tag
Block Data
V
Tag
Block Data
V
Tag
Block Data
mux

## Slide 11: Set-Associative Cache
A set is a group of blocks that can be indexed
A block is first mapped onto a set
  Set index = Block address mod Number of sets in cache
If there are m blocks in a set (m-way set associative) then
  m tags are checked in parallel using m comparators
If 2n sets exist then set index consists of n bits
Cache data size = m  2n+b bytes (with 2b bytes per block)
  Without counting tags and valid bits
A direct-mapped cache has one block per set (m = 1)
A fully-associative cache has one set (2n = 1 or n = 0)

## Slide 12: Set-Associative Cache Diagram
m-way set-associative
V
Tag
Block Data
V
Tag
Block Data
V
Tag
Block Data
V
Tag
Block Data
Address
Tag
Index
offset
Data
=
=
=
=
mux
Hit

## Slide 13: Write Policy
Write Through:
  Writes update cache and lower-level memory
  Cache control bit: only a Valid bit is needed
  Memory always has latest data, which simplifies data coherency
  Can always discard cached data when a block is replaced
Write Back:
  Writes update cache only
  Cache control bits: Valid and Modified bits are required
  Modified cached data is written back to memory when replaced
  Multiple writes to a cache block require only one write to memory
  Uses less memory bandwidth than write-through and less power
  However, more complex to implement than write through

## Slide 14: Write Miss Policy
What happens on a write miss?
Write Allocate:
  Allocate new block in cache
  Write miss acts like a read miss, block is fetched and updated
No Write Allocate:
  Send data to lower-level memory
  Cache is not modified
Typically, write back caches use write allocate
  Hoping subsequent writes will be captured in the cache
Write-through caches often use no-write allocate
  Reasoning: writes must still go to lower level memory

## Slide 15: Write Buffer
Decouples the CPU write from the memory bus writing
  Permits writes to occur without stall cycles until buffer is full
Write-through: all stores are sent to lower level memory
  Write buffer eliminates processor stalls on consecutive writes
Write-back: modified blocks are written when replaced
  Write buffer is used for evicted blocks that must be written back
The address and modified data are written in the buffer
  The write is finished from the CPU perspective
  CPU continues while the write buffer prepares to write memory
If buffer is full, CPU stalls until buffer has an empty entry

## Slide 16: What Happens on a Cache Miss?
Cache sends a miss signal to stall the processor
Decide which cache block to allocate/replace
  One choice only when the cache is directly mapped
  Multiple choices for set-associative or fully-associative cache
If block to be replaced is modified then write it back
  Modified block is moved into a Write Buffer
  Otherwise, block to be replaced can be simply discarded
Transfer the block from lower level memory to this cache
  Set the valid bit and the tag field from the upper address bits
Restart the instruction that caused the cache miss
Miss Penalty: clock cycles to process a cache miss

## Slide 17: Replacement Policy
Which block to be replaced on a cache miss?
No selection alternatives for direct-mapped caches
m blocks per set to choose from for associative caches
Random replacement
  Candidate blocks are randomly selected
  One counter for all sets (0 to m – 1): incremented on every cycle
  On a cache miss replace block specified by counter
First In First Out (FIFO) replacement
  Replace oldest block in set
  One counter per set (0 to m – 1): specifies oldest block to replace
  Counter is incremented on a cache miss

## Slide 18: Replacement Policy – cont’d
Least Recently Used (LRU)
  Replace block that has been unused for the longest time
  Order blocks within a set from least to most recently used
  Update ordering of blocks on each cache hit
  With m blocks per set, there are m! possible permutations
Pure LRU is too costly to implement when m > 2
  m = 2, there are 2 permutations only (a single bit is needed)
  m = 4, there are 4! = 24 possible permutations
  LRU approximation is used in practice
For large m > 4,
Random replacement can be as effective as LRU

## Slide 19: Hit Rate and Miss Rate
Hit Rate = Hits / (Hits + Misses)
Miss Rate = Misses / (Hits + Misses)
I-Cache Miss Rate = Miss rate in the Instruction Cache
D-Cache Miss Rate = Miss rate in the Data Cache
Example:
  Out of 1000 instructions fetched, 150 missed in the I-Cache
  25% are load-store instructions, 50 missed in the D-Cache
  What are the I-cache and D-cache miss rates?
I-Cache Miss Rate = 150 / 1000 = 15%
D-Cache Miss Rate = 50 / (25% × 1000) = 50 / 250 = 20%

## Slide 20: Memory Stall Cycles
The processor stalls on a Cache miss
  When fetching instructions from the Instruction Cache (I-cache)
  When loading or storing data into the Data Cache (D-cache)
Memory stall cycles = Combined Misses  Miss Penalty
Miss Penalty: clock cycles to process a cache miss
Combined Misses = I-Cache Misses + D-Cache Misses
I-Cache Misses = I-Count × I-Cache Miss Rate
D-Cache Misses = LS-Count × D-Cache Miss Rate
LS-Count (Load & Store) = I-Count × LS Frequency
Cache misses are often reported per thousand instructions

## Slide 21: Memory Stall Cycles Per Instruction
Memory Stall Cycles Per Instruction =
Combined Misses Per Instruction × Miss Penalty
Miss Penalty is assumed equal for I-cache & D-cache
Miss Penalty is assumed equal for Load and Store
Combined Misses Per Instruction =
I-Cache Miss Rate + LS Frequency × D-Cache Miss Rate
Therefore, Memory Stall Cycles Per Instruction =
I-Cache Miss Rate × Miss Penalty +
LS Frequency × D-Cache Miss Rate × Miss Penalty

## Slide 22: Example on Memory Stall Cycles
Consider a program with the given characteristics
  Instruction count (I-Count) = 106 instructions
  30% of instructions are loads and stores
  D-cache miss rate is 5% and I-cache miss rate is 1%
  Miss penalty is 100 clock cycles for instruction and data caches
  Compute combined misses per instruction and memory stall cycles
Combined misses per instruction in I-Cache and D-Cache
  1% + 30%  5% = 0.025 combined misses per instruction
  Equal to 25 misses per 1000 instructions
Memory stall cycles
  0.025  100 (miss penalty) = 2.5 stall cycles per instruction
  Total memory stall cycles = 106  2.5 = 2,500,000

## Slide 23: CPU Time with Memory Stall Cycles
CPIPerfectCache = CPI for ideal cache (no cache misses)
CPIMemoryStalls = CPI in the presence of memory stalls
Memory stall cycles increase the CPI
CPU Time = I-Count × CPIMemoryStalls × Clock Cycle
CPIMemoryStalls = CPIPerfectCache + Mem Stalls per Instruction

## Slide 24: Example on CPI with Memory Stalls
A processor has CPI of 1.5 without any memory stalls
  Cache miss rate is 2% for instruction and 5% for data
  20% of instructions are loads and stores
  Cache miss penalty is 100 clock cycles for I-cache and D-cache
What is the impact on the CPI?
Answer:
Mem Stalls per Instruction =
CPIMemoryStalls =
CPIMemoryStalls / CPIPerfectCache =
Processor is 3 times slower due to memory stall cycles
Instruction
data
0.02×100 + 0.2×0.05×100 = 3
1.5 + 3 = 4.5 cycles per instruction
4.5 / 1.5 = 3

## Slide 25: Average Memory Access Time
Average Memory Access Time (AMAT)
AMAT = Hit time + Miss rate × Miss penalty
Time to access a cache for both hits and misses
Example: Find the AMAT for a cache with
  Cache access time (Hit time) of 1 cycle = 2 ns
  Miss penalty of 20 clock cycles
  Miss rate of 0.05 per access
Solution:
  AMAT = 1 + 0.05 × 20 = 2 cycles = 4 ns
  Without the cache, AMAT will be equal to Miss penalty = 20 cycles

## Slide 26: Improving Cache Performance
Average Memory Access Time (AMAT)
AMAT = Hit time + Miss rate * Miss penalty
Used as a framework for optimizations
Reduce the Hit time
  Small and simple caches
Reduce the Miss Rate
  Larger cache size, higher associativity, and larger block size
Reduce the Miss Penalty
  Multilevel caches