## Slide 1: Chapter 2 Instruction: Language of the Computer
2.13 A C Sort Example to Put it All Together
2.14 Arrays versus Pointers

## Slide 2: Swap Procedure
Illustrates use of assembly instructions for a C sort function
Swap procedure (leaf)
§2.13 A C Sort Example to Put It All Together
Parameters:
$a0 = Address of v[]
$a1 = k,
Return address is in $ra
void swap(int v[], int k)
{ int temp;
temp = v[k]
v[k] = v[k+1];
v[k+1] = temp;
}
swap:
sll $t0,$a1,2 # $t0=k*4
add $t0,$t0,$a0 # $t0=v+k*4
lw $t1,0($t0) # $t1=v[k]
lw $t2,4($t0) # $t2=v[k+1]
sw $t2,0($t0) # v[k]=$t2
sw $t1,4($t0) # v[k+1]=$t1
jr $ra # return

## Slide 3: The Sort Procedure in C
Non-leaf (calls swap)
  void sort (int v[], int n)
  {
  int i, j;
  for (i = 0; i < n; i += 1) {
  for (j = i – 1;j >= 0 && v[j] > v[j + 1]; j -= 1)
  {
  swap(v,j);
  }
  }
  }
Parameters:
$a0 = Address of v[]
$a1 = k,
$s0 = i,
$s1 = j,
Return address is in $ra

## Slide 4: The Procedure Body
move $s2, $a0 # save $a0 into $s2
move $s3, $a1 # save $a1 into $s3
move $s0, $zero # i = 0
for1tst: slt $t0, $s0, $s3 # $t0 = 0 if $s0 ≥ $s3 (i ≥ n)
beq $t0, $zero, exit1 # go to exit1 if $s0 ≥ $s3 (i ≥ n)
addi $s1, $s0, –1 # j = i – 1
for2tst: slti $t0, $s1, 0 # $t0 = 1 if $s1 < 0 (j < 0)
bne $t0, $zero, exit2 # go to exit2 if $s1 < 0 (j < 0)
sll $t1, $s1, 2 # $t1 = j * 4
add $t2, $s2, $t1 # $t2 = v + (j * 4)
lw $t3, 0($t2) # $t3 = v[j]
lw $t4, 4($t2) # $t4 = v[j + 1]
slt $t0, $t4, $t3 # $t0 = 0 if $t4 ≥ $t3
beq $t0, $zero, exit2 # go to exit2 if $t4 ≥ $t3
move $a0, $s2 # 1st param of swap is v (old $a0)
move $a1, $s1 # 2nd param of swap is j
jal swap # call swap procedure
addi $s1, $s1, –1 # j –= 1
j for2tst # jump to test of inner loop
exit2: addi $s0, $s0, 1 # i += 1
j for1tst # jump to test of outer loop
Pass params & call
Move params
Inner loop
Outer loop
Inner loop
Outer loop

## Slide 5: The Full Procedure
sort: addi $sp,$sp, –20 # make room on stack for 5 registers
sw $ra, 16($sp) # save $ra on stack
sw $s3,12($sp) # save $s3 on stack
sw $s2, 8($sp) # save $s2 on stack
sw $s1, 4($sp) # save $s1 on stack
sw $s0, 0($sp) # save $s0 on stack
… # procedure body
…
exit1: lw $s0, 0($sp) # restore $s0 from stack
lw $s1, 4($sp) # restore $s1 from stack
lw $s2, 8($sp) # restore $s2 from stack
lw $s3,12($sp) # restore $s3 from stack
lw $ra,16($sp) # restore $ra from stack
addi $sp,$sp, 20 # restore stack pointer
jr $ra # return to calling routine

## Slide 6: Arrays vs. Pointers
Array indexing involves
  Multiplying index by element size
  Adding to array base address
Pointers correspond directly to memory addresses
  Can avoid indexing complexity
§2.14 Arrays versus Pointers

## Slide 7: Example: Clearing and Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 loop1: sll $t1,$t0,2 # $t1 = i * 4 add $t2,$a0,$t1 # $t2 = # &array[i] sw $zero, 0($t2) # array[i] = 0 addi $t0,$t0,1 # i = i + 1 slt $t3,$t0,$a1 # $t3 = # (i < size) bne $t3,$zero,loop1 # if (…) # goto loop1 | move $t0,$a0 # p = & array[0] sll $t1,$a1,2 # $t1 = size * 4 add $t2,$a0,$t1 # $t2 = # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 addi $t0,$t0,4 # p = p + 4 slt $t3,$t0,$t2 # $t3 = #(p<&array[size]) bne $t3,$zero,loop2 # if (…) # goto loop2

## Slide 8: Comparison of Array vs. Pointer
Array
  Must have “multiply” and add inside the loop to adjust index i.
  Each address must be recalculated from the new index.
Pointer
  The pointer can be incremented directly.
  The scaling shift and the array bound addition is outside of the loop, reducing the instructions executed per iteration.
Compiler can achieve same effect as manual use of pointers
  Induction variable elimination
  Better to make program clearer and safer