## Slide 1: Chapter 3: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations
§3.1 Introduction

## Slide 2: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0

## Slide 3: Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand
    Overflow if result sign is 0
  Subtracting –ve from +ve operand
    Overflow if result sign is 1

## Slide 4: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions
  On overflow, invoke exception handler
    Save PC in exception program counter (EPC) register
    Jump to predefined handler address
    mfc0 (move from coprocessor reg) instruction can retrieve EPC value, to return after corrective action

## Slide 5: Multiplication
Unsigned Integer Multiplication
Signed Integer Multiplication
Faster Integer Multiplication
§3.3 Multiplication

## Slide 6: Unsigned Integer Multiplication
Paper and Pencil Example:
Multiplicand 11002 = 12
Multiplier × 11012 = 13
1100
0000
1100
1100
Product 100111002 = 156
m-bit multiplicand × n-bit multiplier = (m+n)-bit product
Accomplished via shifting and addition
Consumes more time and more chip area than addition
Binary multiplication is easy
0 × multiplicand = 0
1 × multiplicand = multiplicand

## Slide 7: Sequential Unsigned Multiplication
Initialize Product = 0
Check each bit of the Multiplier
If Multiplier bit = 1 then Product = Product + Multiplicand
Shifting the multiplicand to the left
Repeat steps 3 & 4
One cycle per iteration (for each bit of the Multiplier)
  Addition and shifting can be done simultaneously

## Slide 8
Sequential Multiplication Algorithm

## Slide 9: Sequential Multiplication Hardware
Initially 0

## Slide 10: Optimized Multiplier
Initialize Product = 0
Check each bit of the Multiplier
If Multiplier bit = 1 then Product = Product + Multiplicand
Rather than shifting the multiplicand to the left
Instead, Shift the Product to the Right
Has the same net effect and produces the same result
Minimizes the hardware resources
One cycle per iteration (for each bit of the Multiplier)
  Addition and shifting can be done simultaneously

## Slide 11: Sequential Multiplication Hardware
Initialize HI = 0
Initialize LO = Multiplier
Final Product = HI and LO registers
Repeat for each bit of Multiplier
= 0
Start
LO[0]?
HI = HI + Multiplicand
32nd Repetition?
Done
= 1
No
Yes
HI = 0, LO=Multiplier
Shift (Carry, HI, LO) Right 1 bit
32-bit ALU
Control
64 bits
32 bits
write
add
LO[0]
Multiplicand
shift right
32 bits
HI
LO
32 bits
carry

## Slide 12: Sequential Multiplier Example
Consider: 11002 × 11012 , Product = 100111002
4-bit multiplicand and multiplier are used in this example
4-bit adder produces a 5-bit sum (with carry)
1 1 0 0
Shift Right (Carry, HI, LO) by 1 bit
0 1 1 1 1 0 0 1
LO[0] = 0 => Do Nothing
1 1 0 0
Shift Right (Carry, HI, LO) by 1 bit
0 0 1 1 0 0 1 1
1 1 0 0
Shift Right (Carry, HI, LO) by 1 bit
0 1 1 0 0 1 1 0
1 1 0 0
Shift Right (Carry, HI, LO) by 1 bit
1 0 0 1 1 1 0 0
2
1 1 0 0
0 0 0 0 1 1 0 1
Initialize (HI = 0, LO = Multiplier)
0
1
3
4
Multiplicand
Product = HI, LO
Carry
Iteration
0
1 1 0 0 1 1 0 1
LO[0] = 1 => ADD
+
0
1 1 1 1 0 0 1 1
LO[0] = 1 => ADD
+
1
0 0 1 1 1 0 0 1
LO[0] = 1 => ADD
+

## Slide 13: Signed Integer Multiplication
So far, we have dealt with unsigned integer multiplication
First Attempt:
  Convert multiplier and multiplicand into positive numbers
    If negative then obtain the 2's complement and remember the sign
  Perform unsigned multiplication
  Compute the sign of the product
  If product sign < 0 then obtain the 2's complement of the product
"No Thinking Method" for Two's Complement Multiplication
  Sign extend both integers to twice as many bits.
  Take the correct number of result bits from the least significant portion of the result.

## Slide 14: Signed Multiplication (No Thinking)
Case 1: Positive Multiplier
Multiplicand 1111 11002 = -4
Multiplier × 0000 01012 = +5
1111 1100
11 1111 00
Product 100 1110 11002 = -20
Case 2: Negative Multiplier
Multiplicand 1111 11002 = -4
Multiplier × 1111 11012 = -3
1111 1100
11 1111 00
111 1110 0
1111 1100
1 1111 100
11 1111 00
111 1110 0
Product 0000 11002 = +12

## Slide 15: Signed Integer Multiplication
Better Version:
  Use the unsigned multiplication hardware
  When shifting right, extend the sign of the product (sign extend partial product)
  If multiplier is negative, the last step should be a subtract
Case 1: Positive Multiplier
Multiplicand 11002 = -4
Multiplier × 01012 = +5
11111100
111100
Product 111011002 = -20
Sign-extension

## Slide 16: Signed Multiplication (Pencil & Paper)
Case 2: Negative Multiplier
Multiplicand 01002 = 4
Multiplier × 11012 = -3
00000100
000100
11100 (2's complement of 0100)
Product 111101002 = -12
Multiplicand 11002 = -4
Multiplier × 11012 = -3
11111100
111100
00100 (2's complement of 1100)
Product 000011002 = +12
Sign-extension
Sign-extension

## Slide 17: Sequential Signed Multiplier
ALU produces 32-bit result + Sign bit
Check for overflow
  No overflow  Extend sign-bit of result
  Overflow  Invert sign bit
= 0
Start
LO[0]?
First 31 iterations: HI = HI + Multiplicand
Last iteration: HI = HI – Multiplicand
32nd Repetition?
Done
= 1
No
Yes
HI = 0, LO = Multiplier
Shift Right (Sign, HI, LO) 1 bit
32-bit ALU
Control
64 bits
32 bits
write
add, sub
LO[0]
Multiplicand
shift right
32 bits
HI
LO
32 bits
sign

## Slide 18: Signed Multiplication Example
Consider: 11002 (-4) × 11012 (-3), Product = 000011002
Check for overflow: No overflow  Extend sign bit
Last iteration: add 2's complement of Multiplicand
1 1 0 0
Shift (Sign, HI, LO) right 1 bit
1 1 0 1 1 0 0 1
LO[0] = 0 => Do Nothing
1 1 0 0
Shift (Sign, HI, LO) right 1 bit
1 1 1 1 0 0 1 1
1 1 0 0
Shift (Sign, HI, LO) right 1 bit
1 1 1 0 0 1 1 0
Shift (Sign, HI, LO) right 1 bit
0 0 0 0 1 1 0 0
2
1 1 0 0
0 0 0 0 1 1 0 1
Initialize (HI = 0, LO = Multiplier)
0
1
3
4
Multiplicand
Product = HI, LO
Sign
Iteration
1
1 1 0 0 1 1 0 1
LO[0] = 1 => ADD
+
1
1 0 1 1 0 0 1 1
LO[0] = 1 => ADD
+
0 1 0 0
0
0 0 0 1 1 0 0 1
LO[0] = 1 => SUB (ADD 2's compl)
+

## Slide 19: Faster Integer Multiplier
Uses Multiple Adders (Cost vs. Performance)
Can be pipelined

## Slide 20: Unsigned Division (Paper & Pencil)
Try to see how big a number can be subtracted, creating a digit of the quotient on each attempt
= 19 Quotient
Divisor 10112 110110012 = 217 Dividend
-1011
10
101
1010
10100
-1011
1001
10011
-1011
10002 = 8 Remainder
Binary division is accomplished via shifting and subtraction
Dividend =
Quotient × Divisor
+ Remainder
217 = 19 × 11 + 8
1
0
0
1
12
§3.4 Division

## Slide 21: Division Hardware
Initially dividend
Initially divisor in left half
A comparison requires a subtract; the sign of the result is examined; if the result is negative, the divisor must be added back

## Slide 22: Divide Example
Divide 7ten (0000 0111two) by 2ten (0010two)
Iter | Step | Quot | Divisor | Remainder
0 | Initial values | 0000 | 0010 0000 | 0000 0111
1 | Rem = Rem – Div Rem < 0  +Div, shift 0 into Q Shift Div right | 0000 0000 0000 | 0010 0000 0010 0000 0001 0000 | 1110 0111 0000 0111 0000 0111
2 | Same steps as 1 | 0000 0000 0000 | 0001 0000 0001 0000 0000 1000 | 1111 0111 0000 0111 0000 0111
3 | Same steps as 1 | 0000 | 0000 0100 | 0000 0111
4 | Rem = Rem – Div Rem >= 0  shift 1 into Q Shift Div right | 0000 0001 0001 | 0000 0100 0000 0100 0000 0010 | 0000 0011 0000 0011 0000 0011
5 | Same steps as 4 | 0011 | 0000 0001 | 0000 0001

## Slide 23: Efficient Sequential Division
Uses two registers: HI and LO
Initialize: HI = Remainder = 0 and LO = Dividend
Shift (HI, LO) LEFT by 1 bit (also Shift Quotient LEFT)
  Shift the remainder and dividend registers together LEFT
  Has the same net effect of shifting the divisor RIGHT
Compute: Difference = Remainder – Divisor
If (Difference ≥ 0) then
  Remainder = Difference
  Set Least significant Bit of Quotient
Observation to Reduce Hardware:
  LO register can be also used to store the computed Quotient

## Slide 24: Sequential Division Hardware
Initialize:
  HI = 0, LO = Dividend
Results:
  HI = Remainder
  LO = Quotient
Start
Difference?
2. HI = Remainder = Difference
Set least significant bit of LO
32nd Repetition?
Done
< 0
≥ 0
No
Yes
Shift (HI, LO) Left
Difference = HI – Divisor
shift left
Divisor
32-bit ALU
LO
32 bits
write
sub
32 bits
Difference
sign
set lsb
HI
32 bits
Control

## Slide 25: Unsigned Integer Division Example
2: Diff < 0 => Do Nothing
Example: 11102 / 00112 (4-bit dividend & divisor)
Result Quotient = 01002 and Remainder = 00102
4-bit registers for Remainder and Divisor (4-bit ALU)
2: Rem = Diff, set lsb of LO
1 0 0 1
0 0 0 0
2: Diff < 0 => Do Nothing
2: Diff < 0 => Do Nothing
2
0 0 0 0
1 1 1 0
Initialize
0
1
3
4
HI
Difference
LO
Iteration
0 0 1 1
Divisor
1 1 1 0
1: Shift Left, Diff = HI - Divisor
0 0 0 1
1 1 0 0
0 0 1 1
0 0 0 0
1: Shift Left, Diff = HI - Divisor
0 0 1 1
1 0 0 0
0 0 1 1
1 1 1 0
1: Shift Left, Diff = HI - Divisor
0 0 0 1
0 0 1 0
0 0 1 1
1 1 1 1
1: Shift Left, Diff = HI - Divisor
0 0 1 0
0 1 0 0
0 0 1 1

## Slide 26: Signed Integer Division
Simplest way is to remember the signs
Convert the dividend and divisor to positive
  Obtain the 2's complement if they are negative
Do the unsigned division
Compute the signs of the quotient and remainder
  Quotient sign = Dividend sign XOR Divisor sign
  Remainder sign = Dividend sign
Negate the quotient and remainder if their sign is negative
  Obtain the 2's complement to convert them to negative

## Slide 27: Signed Integer Division Examples
Positive Dividend and Positive Divisor
  Example: +17 / +3 Quotient = +5 Remainder = +2
Positive Dividend and Negative Divisor
  Example: +17 / –3 Quotient = –5 Remainder = +2
Negative Dividend and Positive Divisor
  Example: –17 / +3 Quotient = –5 Remainder = –2
Negative Dividend and Negative Divisor
  Example: –17 / –3 Quotient = +5 Remainder = –2
The following equation must always hold:
Dividend = Quotient × Divisor + Remainder
Compute the signs of the quotient and remainder
  Quotient sign = Dividend sign XOR Divisor sign
  Remainder sign = Dividend sign

## Slide 28: Integer Multiplication in MIPS
Multiply instructions
  mult $s1,$s2 Signed multiplication
  multu $s1,$s2 Unsigned multiplication
32-bit multiplication produces a 64-bit Product
Separate pair of 32-bit registers
  HI = high-order 32-bit of product
  LO = low-order 32-bit of product
MIPS also has a special mul instruction
  mul $s0,$s1,$s2 $s0 = $s1 × $s2
  Put low-order 32 bits into destination register
  HI & LO are undefined
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 29: Integer Division in MIPS
Divide instructions
  div $s1,$s2 Signed division
  divu $s1,$s2 Unsigned division
Division produces quotient and remainder
Separate pair of 32-bit registers
  HI = 32-bit remainder
  LO = 32-bit quotient
No overflow or divide-by-0 checking
  If divisor is 0 then result is unpredictable
  Software must perform checks if required
Use mfhi, mflo to access result
  mfhi Rd (move from HI to Rd)
  mflo Rd (move from LO to Rd)
Multiply
Divide
$0
HI
LO
$1
.
.
$31

## Slide 30: Integer Multiply/Divide Instructions
Instruction | Meaning | Format |  |  |  |  | 
mult Rs, Rt | Hi, Lo = Rs × Rt | op6 = 0 | Rs5 | Rt5 | 0 | 0 | 0x18
multu Rs, Rt | Hi, Lo = Rs × Rt | op6 = 0 | Rs5 | Rt5 | 0 | 0 | 0x19
mul Rd, Rs, Rt | Rd = Rs × Rt | 0x1c | Rs5 | Rt5 | Rd5 | 0 | 0x02
div Rs, Rt | Hi, Lo = Rs / Rt | op6 = 0 | Rs5 | Rt5 | 0 | 0 | 0x1a
divu Rs, Rt | Hi, Lo = Rs / Rt | op6 = 0 | Rs5 | Rt5 | 0 | 0 | 0x1b
mfhi Rd | Rd = Hi | op6 = 0 | 0 | 0 | Rd5 | 0 | 0x10
mflo Rd | Rd = Lo | op6 = 0 | 0 | 0 | Rd5 | 0 | 0x12
Signed arithmetic: mult, div (Rs and Rt are signed)
  LO = 32-bit low-order and HI = 32-bit high-order of multiplication
  LO = 32-bit quotient and HI = 32-bit remainder of division
Unsigned arithmetic: multu, divu (Rs and Rt are unsigned)
NO arithmetic exception can occur

## Slide 31: Integer to String Conversion
Objective: convert an unsigned 32-bit integer to a string
How to obtain the decimal digits of the number?
  Divide the number by 10, Remainder = decimal digit (0 to 9)
  Convert decimal digit into its ASCII representation ('0' to '9')
  Repeat the division until the quotient becomes zero
  Digits are computed backwards from least to most significant
Example: convert 2037 to a string
  Divide 2037/10 quotient = 203 remainder = 7 char = '7'
  Divide 203/10 quotient = 20 remainder = 3 char = '3'
  Divide 20/10 quotient = 2 remainder = 0 char = '0'
  Divide 2/10 quotient = 0 remainder = 2 char = '2'

## Slide 32: Integer to String Procedure
#--------------------------------------------------------------
# int2str: Converts an unsigned integer into a string
# Input: $a0 = unsigned integer
# In/Out: $a1 = address of string buffer (12 bytes)
#--------------------------------------------------------------
int2str:
move $t0, $a0 # $t0 = dividend = unsigned integer
li $t1, 10 # $t1 = divisor = 10
addiu $a1, $a1, 11 # start at end of string buffer
sb $zero, 0($a1) # store a NULL byte
convert:
divu $t0, $t1 # LO = quotient, HI = remainder
mflo $t0 # $t0 = quotient
mfhi $t2 # $t2 = remainder
addiu $t2, $t2, 0x30 # convert digit to a character
addiu $a1, $a1, -1 # point to previous byte
sb $t2, 0($a1) # store digit character
bnez $t0, convert # loop if quotient is not 0
jr $ra # return to caller

## Slide 33: Floating Point
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
MIPS Floating-Point Instructions
§3.5 Floating Point

## Slide 34: The World is Not Just Integers
Programming languages support numbers with fraction
  Called floating-point numbers
  Examples:
  3.14159265… (π)
  2.71828… (e)
  0.000000001 or 1.0 × 10–9 (seconds in a nanosecond)
  86,400,000,000,000 or 8.64 × 1013 (nanoseconds in a day)
  last number is a large integer that cannot fit in a 32-bit integer
We use a scientific notation to represent
  Very small numbers (e.g. 1.0 × 10–9)
  Very large numbers (e.g. 8.64 × 1013)
  Scientific notation: ± d . f1f2f3f4 … × 10 ± e1e2e3

## Slide 35: Floating-Point Numbers
Examples of floating-point numbers in base 10 …
  5.341×103 , 0.05341×105 , –2.013×10–1 , –201.3×10–3
Examples of floating-point numbers in base 2 …
  1.00101×223 , 0.0100101×225 , –1.101101×2–3 , –1101.101×2–6
  Exponents are kept in decimal for clarity
  The binary number (1101.101)2 = 23+22+20+2–1+2–3 = 13.625
Floating-point numbers should be normalized
  Exactly one non-zero digit should appear before the point
    In a decimal number, this digit can be from 1 to 9
    In a binary number, this digit should be 1
      ±1.xxxxxxx2 × 2yyyy
  Normalized FP Numbers: 5.341×103 and –1.101101×2–3
  NOT Normalized: 0.05341×105 and –1101.101×2–6
decimal point
binary point

## Slide 36: Floating-Point Representation
A floating-point number is represented by the triple
  S is the Sign bit (0 is positive and 1 is negative)
    Representation is called sign and magnitude
  E is the Exponent field (signed)
    Very large numbers have large positive exponents
    Very small close-to-zero numbers have negative exponents
    More bits in exponent field increases range of values
  F is the Fraction field (fraction after binary point)
    More bits in fraction field improves the precision of FP numbers
Value of a floating-point number = (-1)S × val(F) × 2val(E)
S
Exponent
Fraction

## Slide 37: Next . . .
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
MIPS Floating-Point Instructions

## Slide 38: IEEE 754 Floating-Point Standard
Found in virtually every computer invented since 1980
  Simplified porting of floating-point numbers
  Unified the development of floating-point algorithms
  Increased the accuracy of floating-point numbers
Single Precision Floating Point Numbers (32 bits)
  1-bit sign + 8-bit exponent + 23-bit fraction
Double Precision Floating Point Numbers (64 bits)
  1-bit sign + 11-bit exponent + 52-bit fraction
S
Exponent8
Fraction23
S
Exponent11
Fraction52
(continued)

## Slide 39: Normalized Floating Point Numbers
For a normalized floating point number (S, E, F)
Significand is equal to (1.F)2 = (1.f1f2f3f4…)2
  IEEE 754 assumes hidden 1. (not stored) for normalized numbers
  Significand is 1 bit longer than fraction
Value of a Normalized Floating Point Number is
(–1)S × (1.F)2 × 2val(E)
(–1)S × (1.f1f2f3f4 …)2 × 2val(E)
(–1)S × (1 + f1×2-1 + f2×2-2 + f3×2-3 + f4×2-4 …)2 × 2val(E)
(–1)S is 1 when S is 0 (positive), and –1 when S is 1 (negative)
S
E
F = f1 f2 f3 f4 …

## Slide 40: Biased Exponent Representation
How to represent a signed exponent? Choices are …
  Sign + magnitude representation for the exponent
  Two’s complement representation
  Biased representation
IEEE 754 uses biased representation for the exponent
  Value of exponent = val(E) = E – Bias (Bias is a constant)
Recall that exponent field is 8 bits for single precision
  E can be in the range 0 to 255
  E = 0 and E = 255 are reserved for special use (discussed later)
  E = 1 to 254 are used for normalized floating point numbers
  Bias = 127 (half of 254), val(E) = E – 127
  val(E=1) = –126, val(E=127) = 0, val(E=254) = 127

## Slide 41: Biased Exponent – Cont’d
For double precision, exponent field is 11 bits
  E can be in the range 0 to 2047
  E = 0 and E = 2047 are reserved for special use
  E = 1 to 2046 are used for normalized floating point numbers
  Bias = 1023 (half of 2046), val(E) = E – 1023
  val(E=1) = –1022, val(E=1023) = 0, val(E=2046) = 1023
Value of a Normalized Floating Point Number is
(–1)S × (1.F)2 × 2E – Bias
(–1)S × (1.f1f2f3f4 …)2 × 2E – Bias
(–1)S × (1 + f1×2-1 + f2×2-2 + f3×2-3 + f4×2-4 …)2 × 2E – Bias

## Slide 42: Examples of Single Precision Float
What is the decimal value of this Single Precision float?
Solution:
  Sign = 1 is negative
  Exponent = (01111100)2 = 124, E – bias = 124 – 127 = –3
  Significand = (1.0100 … 0)2 = 1 + 2-2 = 1.25 (1. is implicit)
  Value in decimal = –1.25 × 2–3 = –0.15625
What is the decimal value of?
Solution:
  Value in decimal = +(1.01001100 … 0)2 × 2130–127 =
  (1.01001100 … 0)2 × 23 = (1010.01100 … 0)2 = 10.375
1
0
1
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
1
0
0
1
0
0
1
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
implicit

## Slide 43: Examples of Double Precision Float
What is the decimal value of this Double Precision float ?
Solution:
  Value of exponent = (10000000101)2 – Bias = 1029 – 1023 = 6
  Value of double float = (1.00101010 … 0)2 × 26 (1. is implicit) =
  (1001010.10 … 0)2 = 74.5
What is the decimal value of ?
Do it yourself! (answer should be –1.5 × 2–7 = –0.01171875)
0
1
0
0
0
0
0
0
0
1
0
1
0
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 44: Converting FP Decimal to Binary
Convert –0.8125 to binary in single and double precision
Solution:
  Fraction bits can be obtained using multiplication by 2
    0.8125 × 2 = 1.625
    0.625 × 2 = 1.25
    0.25 × 2 = 0.5
    0.5 × 2 = 1.0
    Stop when fractional part is 0
  Fraction = (0.1101)2 = (1.101)2 × 2 –1 (Normalized)
  Exponent = –1 + Bias = 126 (single precision) and 1022 (double)
0.8125 = (0.1101)2 = ½ + ¼ + 1/16 = 13/16
1
0
1
1
1
1
1
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
1
1
1
1
1
1
1
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Single Precision
Double Precision

## Slide 45: Largest Normalized Float
What is the Largest normalized float?
Solution for Single Precision:
  Exponent – bias = 254 – 127 = 127 (largest exponent for SP)
  Significand = (1.111 … 1)2 = almost 2
  Value in decimal ≈ 2 × 2127 ≈ 2128 ≈ 3.4028 … × 1038
Solution for Double Precision:
  Value in decimal ≈ 2 × 21023 ≈ 21024 ≈ 1.79769 … × 10308
Overflow: exponent is too large to fit in the exponent field
0
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 46: Smallest Normalized Float
What is the smallest (in absolute value) normalized float?
Solution for Single Precision:
  Exponent – bias = 1 – 127 = –126 (smallest exponent for SP)
  Significand = (1.000 … 0)2 = 1
  Value in decimal = 1 × 2–126 = 1.17549 … × 10–38
Solution for Double Precision:
  Value in decimal = 1 × 2–1022 = 2.22507 … × 10–308
Underflow: exponent is too small to fit in exponent field
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 47: Zero, Infinity, and NaN
Zero
  Exponent field E = 0 and fraction F = 0
  +0 and –0 are possible according to sign bit S
Infinity
  Infinity is a special value represented with maximum E and F = 0
    For single precision with 8-bit exponent: maximum E = 255
    For double precision with 11-bit exponent: maximum E = 2047
  Infinity can result from overflow or division by zero
  +∞ and –∞ are possible according to sign bit S
NaN (Not a Number)
  NaN is a special value represented with maximum E and F ≠ 0
  Result from exceptional situations, such as 0/0 or sqrt(negative)
  Operation on a NaN results is NaN: Op(X, NaN) = NaN

## Slide 48: Denormalized Numbers
IEEE standard uses denormalized numbers to …
  Fill the gap between 0 and the smallest normalized float
  Provide gradual underflow to zero
Denormalized: exponent field E is 0 and fraction F ≠ 0
  Implicit 1. before the fraction now becomes 0. (not normalized)
Value of denormalized number ( S, 0, F )
Single precision: (–1) S × (0.F)2 × 2–126
Double precision: (–1) S × (0.F)2 × 2–1022
Denorm
Denorm
+∞
Positive
Overflow
-∞
Negative
Overflow
Negative
Underflow
Positive
Underflow
Normalized (–ve)
Normalized (+ve)
2–126
2128
0
-2128
-2–126

## Slide 49: Summary of IEEE 754 Encoding
Single-Precision | Exponent = 8 | Fraction = 23 | Value
Normalized Number | 1 to 254 | Anything | ± (1.F)2 × 2E – 127
Denormalized Number | 0 | nonzero | ± (0.F)2 × 2–126
Zero | 0 | 0 | ± 0
Infinity | 255 | 0 | ± ∞
NaN | 255 | nonzero | NaN
Double-Precision | Exponent = 11 | Fraction = 52 | Value
Normalized Number | 1 to 2046 | Anything | ± (1.F)2 × 2E – 1023
Denormalized Number | 0 | nonzero | ± (0.F)2 × 2–1022
Zero | 0 | 0 | ± 0
Infinity | 2047 | 0 | ± ∞
NaN | 2047 | nonzero | NaN

## Slide 50: Floating-Point Comparison
IEEE 754 floating point numbers are ordered
  Because exponent uses a biased representation …
    Exponent value and its binary representation have same ordering
  Placing exponent before the fraction field orders the magnitude
    Larger exponent  larger magnitude
    For equal exponents, Larger fraction  larger magnitude
    0 < (0.F)2 × 2Emin < (1.F)2 × 2E–Bias < ∞ (Emin = 1 – Bias)
  Because sign bit is most significant  quick test of signed <
Integer comparator can compare magnitudes
Integer
Magnitude
Comparator
X < Y
X = Y
X > Y
X = (EX , FX)
Y = (EY , FY)

## Slide 51: Next . . .
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
MIPS Floating-Point Instructions

## Slide 52: Floating Point Addition Example
Consider Adding (Single-Precision Floating-Point):
  + 1.111001000000000000000102 × 24
  + 1.100000000000001100001012 × 22
Cannot add significands … Why?
  Because exponents are not equal
How to make exponents equal?
  Shift the significand of the lesser exponent right
  Difference between the two exponents = 4 – 2 = 2
  So, shift right second number by 2 bits and increment exponent
  1.100000000000001100001012 × 22
  = 0.01100000000000001100001 012 × 24

## Slide 53: Floating-Point Addition – cont'd
Now, ADD the Significands:
+ 1.11100100000000000000010 × 24
+ 1.10000000000000110000101 × 22
+ 1.11100100000000000000010 × 24
+ 0.01100000000000001100001 01 × 24 (shift right)
+10.01000100000000001100011 01 × 24 (result)
Addition produces a carry bit, result is NOT normalized
Normalize Result (shift right and increment exponent):
+ 10.01000100000000001100011 01 × 24
= + 1.00100010000000000110001 101 × 25

## Slide 54: Rounding
Single-precision requires only 23 fraction bits
However, Normalized result can contain additional bits
1.00100010000000000110001 | 1 01 × 25
Two extra bits are needed for rounding
  Round bit: appears just after the normalized result
  Sticky bit: appears after the round bit (OR of all additional bits)
Since RS = 11, increment fraction to round to nearest
    1.00100010000000000110001 × 25
    +1
    1.00100010000000000110010 × 25 (Rounded)
Round Bit: R = 1
Sticky Bit: S = 1

## Slide 55: Floating-Point Subtraction Example
Sometimes, addition is converted into subtraction
  If the sign bits of the operands are different
Consider Adding:
+ 1.00000000101100010001101 × 2-6
– 1.00000000000000010011010 × 2-1
+ 0.00001000000001011000100 01101 × 2-1 (shift right 5 bits)
– 1.00000000000000010011010 × 2-1
0 0.00001000000001011000100 01101 × 2-1
1 0.11111111111111101100110 × 2-1 (2's complement)
1 1.00001000000001000101010 01101 × 2-1 (ADD)
- 0.11110111111110111010101 10011 × 2-1 (2's complement)
2's complement of result is required if result is negative

## Slide 56: Floating-Point Subtraction – cont'd
+ 1.00000000101100010001101 × 2-6
– 1.00000000000000010011010 × 2-1
- 0.11110111111110111010101 10011 × 2-1 (result is negative)
Result should be normalized
  For subtraction, we can have leading zeros. To normalize, count the number of leading zeros, then shift result left and decrement the exponent accordingly.
- 0.11110111111110111010101 1 0011 × 2-1
- 1.11101111111101110101011 0011 × 2-2 (Normalized)
Guard bit
Guard bit: guards against loss of a fraction bit
  Needed for subtraction, when result has a leading zero and should be normalized.

## Slide 57: Floating-Point Subtraction – cont'd
Next, normalized result should be rounded
- 0.11110111111110111010101 1 0 011 × 2-1
- 1.11101111111101110101011 0 011 × 2-2 (Normalized)
Guard bit
Round bit: R=0
Sticky bit: S = 1
Since R = 0, it is more accurate to truncate the result even if S = 1. We simply discard the extra bits.
- 1.11101111111101110101011 0 011 × 2-2 (Normalized)
- 1.11101111111101110101011 × 2-2 (Rounded to nearest)
IEEE 754 Representation of Result
1
0
1
1
1
1
1
0
1
1
1
1
0
1
1
1
1
1
1
1
1
0
1
1
1
0
1
0
1
0
1
1

## Slide 58: Rounding to Nearest Even
Normalized result has the form: 1. f1 f2 … fl R S
  The round bit R appears after the last fraction bit fl
  The sticky bit S is the OR of all remaining additional bits
Round to Nearest Even: default rounding mode
Four cases for RS:
  RS = 00  Result is Exact, no need for rounding
  RS = 01  Truncate result by discarding RS
  RS = 11  Increment result: ADD 1 to last fraction bit
  RS = 10  Tie Case (either truncate or increment result)
    Check Last fraction bit fl (f23 for single-precision or f52 for double)
    If fl is 0 then truncate result to keep fraction even
    If fl is 1 then increment result to make fraction even

## Slide 59: Additional Rounding Modes
IEEE 754 standard specifies four rounding modes:
Round to Nearest Even: described in previous slide
Round toward +Infinity: result is rounded up
  Increment result if sign is positive and R or S = 1
Round toward -Infinity: result is rounded down
  Increment result if sign is negative and R or S = 1
Round toward 0: always truncate result
Rounding or Incrementing result might generate a carry
  This occurs when all fraction bits are 1
  Re-Normalize after Rounding step is required only in this case

## Slide 60: Example on Rounding
Round following result using IEEE 754 rounding modes:
–1.11111111111111111111111 1 0 × 2-7
Round to Nearest Even:
  Increment result since RS = 10 and f23 = 1
  Incremented result: –10.00000000000000000000000 × 2-7
  Renormalize and increment exponent (because of carry)
  Final rounded result: –1.00000000000000000000000 × 2-6
Round towards +∞:
  Truncated Result: –1.11111111111111111111111 × 2-7
Round towards –∞:
  Final rounded result: –1.00000000000000000000000 × 2-6
Round towards 0:
Round Bit
Sticky Bit
Truncate result since negative
Increment since negative and R = 1
Truncate always

## Slide 61: Floating Point Addition / Subtraction
1. Compare the exponents of the two numbers. Shift the smaller number to the right until its exponent would match the larger exponent.
2. Add / Subtract the significands according to the sign bits.
3. Normalize the sum, either shifting right and incrementing the exponent or shifting left and decrementing the exponent
4. Round the significand to the appropriate number of bits, and renormalize if rounding generates a carry
Start
Done
Overflow or
underflow?
Exception
yes
no
Shift significand right by
d = | EX – EY |
Add significands when signs
of X and Y are identical,
Subtract when different
X – Y becomes X + (–Y)
Normalization shifts right by 1 if there is a carry, or shifts left by the number of leading zeros in the case of subtraction
Rounding either truncates fraction, or adds a 1 to least significant fraction bit

## Slide 62: Floating Point Adder Block Diagram
c
z
EZ
EX
FX
Shift Right / Left
Inc / Dec
EY
Swap
FY
Shift Right
Exponent
Subtractor
Significand
Adder/Subtractor
1
1
sign
Sign
Computation
d = | EX – EY |
max ( EX , EY )
add / subtract
Rounding Logic
sign
SY
add/sub
FZ
SZ
c
SX
z
Detect carry, or
Count leading 0’s
c
0 1

## Slide 63: Next . . .
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
MIPS Floating-Point Instructions

## Slide 64: Floating Point Multiplication Example
Consider multiplying:
-1.110 1000 0100 0000 1010 00012 × 2–4
× 1.100 0000 0001 0000 0000 00002 × 2–2
Unlike addition, we add the exponents of the operands
  Result exponent value = (–4) + (–2) = –6
Using the biased representation: EZ = EX + EY – Bias
  EX = (–4) + 127 = 123 (Bias = 127 for single precision)
  EY = (–2) + 127 = 125
  EZ = 123 + 125 – 127 = 121 (value = –6)
Sign bit of product can be computed independently
Sign bit of product = SignX XOR SignY = 1 (negative)

## Slide 65: Floating-Point Multiplication, cont'd
Now multiply the significands:
(Multiplicand) 1.11010000100000010100001
(Multiplier) × 1.10000000001000000000000
111010000100000010100001
111010000100000010100001
1.11010000100000010100001
10.1011100011111011111100110010100001000000000000
24 bits × 24 bits  48 bits (double number of bits)
Multiplicand × 0 = 0 Zero rows are eliminated
Multiplicand × 1 = Multiplicand (shifted left)

## Slide 66: Floating-Point Multiplication, cont'd
Normalize Product:
-10.10111000111110111111001100... × 2-6
Shift right and increment exponent because of carry bit
= -1.010111000111110111111001100... × 2-5
Round to Nearest Even: (keep only 23 fraction bits)
1.01011100011111011111100 | 1 100... × 2-5
Round bit = 1, Sticky bit = 1, so increment fraction
Final result = -1.01011100011111011111101 × 2-5
IEEE 754 Representation
1
0
1
1
1
1
0
1
0
0
1
0
1
1
1
0
0
0
1
1
1
1
1
0
1
1
1
1
1
1
0
1

## Slide 67: Floating Point Multiplication
1. Add the biased exponents of the two numbers, subtracting the bias from the sum to get the new biased exponent
Multiply the significands. Set the result sign to positive if operands have same sign, and negative otherwise
3. Normalize the product if necessary, shifting its significand right and incrementing the exponent
4. Round the significand to the appropriate number of bits, and renormalize if rounding generates a carry
Start
Done
Overflow or
underflow?
Exception
yes
no
Biased Exponent Addition
EZ = EX + EY – Bias
Result sign SZ = SX xor SY can be computed independently
Since the operand significands 1.FX and 1.FY are ≥ 1 and < 2, their product is ≥ 1 and < 4.
To normalize product, we need to shift right at most by 1 bit and increment exponent
Rounding either truncates fraction, or adds a 1 to least significant fraction bit

## Slide 68: Extra Bits to Maintain Precision
Floating-point numbers are approximations for …
  Real numbers that they cannot represent
Infinite variety of real numbers exist between 1.0 and 2.0
  However, exactly 223 fractions represented in Single Precision
  Exactly 252 fractions can be represented in Double Precision
Extra bits are generated in intermediate results when …
  Shifting and adding/subtracting a p-bit significand
  Multiplying two p-bit significands (product is 2p bits)
But when packing result fraction, extra bits are discarded
Few extra bits are needed: guard, round, and sticky bits
Minimize hardware but without compromising accuracy

## Slide 69: Advantages of IEEE 754 Standard
Used predominantly by the industry
Encoding of exponent and fraction simplifies comparison
  Integer comparator used to compare magnitude of FP numbers
Includes special exceptional values: NaN and ±∞
  Special rules are used such as:
    0/0 is NaN, sqrt(–1) is NaN, 1/0 is ∞, and 1/∞ is 0
  Computation may continue in the face of exceptional conditions
Denormalized numbers to fill the gap
  Between smallest normalized number 1.0 × 2Emin and zero
  Denormalized numbers , values 0.F × 2Emin , are closer to zero
  Gradual underflow to zero

## Slide 70: Next . . .
Floating-Point Numbers
IEEE 754 Floating-Point Standard
Floating-Point Addition and Subtraction
Floating-Point Multiplication
MIPS Floating-Point Instructions

## Slide 71: MIPS Floating Point Coprocessor
Called Coprocessor 1 or the Floating Point Unit (FPU)
32 separate floating point registers: $f0, $f1, …, $f31
FP registers are 32 bits for single precision numbers
Paired for double-precision: $f0/$f1, $f2/$f3, …
Use the even number for double precision registers
  $f0, $f2, $f4, …, $f30 are used for double precision
Separate FP instructions for single/double precision
  Single precision: add.s, sub.s, mul.s, div.s (.s extension)
  Double precision: add.d, sub.d, mul.d, div.d (.d extension)
FP instructions are more complex than the integer ones
  Take more cycles to execute

## Slide 72: FP Arithmetic Instructions
Instruction | Meaning | Format |  |  |  |  | 
add.s fd, fs, ft | (fd) = (fs) + (ft) | 0x11 | 0 | ft5 | fs5 | fd5 | 0
add.d fd, fs, ft | (fd) = (fs) + (ft) | 0x11 | 1 | ft5 | fs5 | fd5 | 0
sub.s fd, fs, ft | (fd) = (fs) – (ft) | 0x11 | 0 | ft5 | fs5 | fd5 | 1
sub.d fd, fs, ft | (fd) = (fs) – (ft) | 0x11 | 1 | ft5 | fs5 | fd5 | 1
mul.s fd, fs, ft | (fd) = (fs) × (ft) | 0x11 | 0 | ft5 | fs5 | fd5 | 2
mul.d fd, fs, ft | (fd) = (fs) × (ft) | 0x11 | 1 | ft5 | fs5 | fd5 | 2
div.s fd, fs, ft | (fd) = (fs) / (ft) | 0x11 | 0 | ft5 | fs5 | fd5 | 3
div.d fd, fs, ft | (fd) = (fs) / (ft) | 0x11 | 1 | ft5 | fs5 | fd5 | 3
sqrt.s fd, fs | (fd) = sqrt (fs) | 0x11 | 0 | 0 | fs5 | fd5 | 4
sqrt.d fd, fs | (fd) = sqrt (fs) | 0x11 | 1 | 0 | fs5 | fd5 | 4
abs.s fd, fs | (fd) = abs (fs) | 0x11 | 0 | 0 | fs5 | fd5 | 5
abs.d fd, fs | (fd) = abs (fs) | 0x11 | 1 | 0 | fs5 | fd5 | 5
neg.s fd, fs | (fd) = – (fs) | 0x11 | 0 | 0 | fs5 | fd5 | 7
neg.d fd, fs | (fd) = – (fs) | 0x11 | 1 | 0 | fs5 | fd5 | 7

## Slide 73: FP Load/Store Instructions
Separate floating point load/store instructions
  lwc1: load word coprocessor 1
  ldc1: load double coprocessor 1
  swc1: store word coprocessor 1
  sdc1: store double coprocessor 1
Better names can be used for the above instructions
  l.s = lwc1 (load FP single), l.d = ldc1 (load FP double)
  s.s = swc1 (store FP single), s.d = sdc1 (store FP double)
Instruction | Meaning | Format |  |  | 
lwc1 $f2, 40($t0) | ($f2) = Mem[($t0)+40] | 0x31 | $t0 | $f2 | im16 = 40
ldc1 $f2, 40($t0) | ($f2) = Mem[($t0)+40] | 0x35 | $t0 | $f2 | im16 = 40
swc1 $f2, 40($t0) | Mem[($t0)+40] = ($f2) | 0x39 | $t0 | $f2 | im16 = 40
sdc1 $f2, 40($t0) | Mem[($t0)+40] = ($f2) | 0x3d | $t0 | $f2 | im16 = 40
General purpose register is used as the base register

## Slide 74: FP Data Movement Instructions
Moving data between general purpose and FP registers
  mfc1: move from coprocessor 1 (to general purpose register)
  mtc1: move to coprocessor 1 (from general purpose register)
Moving data between FP registers
  mov.s: move single precision float
  mov.d: move double precision float = even/odd pair of registers
Instruction | Meaning | Format |  |  |  |  | 
mfc1 $t0, $f2 | ($t0) = ($f2) | 0x11 | 0 | $t0 | $f2 | 0 | 0
mtc1 $t0, $f2 | ($f2) = ($t0) | 0x11 | 4 | $t0 | $f2 | 0 | 0
mov.s $f4, $f2 | ($f4) = ($f2) | 0x11 | 0 | 0 | $f2 | $f4 | 6
mov.d $f4, $f2 | ($f4) = ($f2) | 0x11 | 1 | 0 | $f2 | $f4 | 6

## Slide 75: FP Convert Instructions
Instruction | Meaning | Format |  |  |  |  | 
cvt.s.w fd, fs | to single from integer | 0x11 | 0 | 0 | fs5 | fd5 | 0x20
cvt.s.d fd, fs | to single from double | 0x11 | 1 | 0 | fs5 | fd5 | 0x20
cvt.d.w fd, fs | to double from integer | 0x11 | 0 | 0 | fs5 | fd5 | 0x21
cvt.d.s fd, fs | to double from single | 0x11 | 1 | 0 | fs5 | fd5 | 0x21
cvt.w.s fd, fs | to integer from single | 0x11 | 0 | 0 | fs5 | fd5 | 0x24
cvt.w.d fd, fs | to integer from double | 0x11 | 1 | 0 | fs5 | fd5 | 0x24
Convert instruction: cvt.x.y
  Convert to destination format x from source format y
Supported formats
  Single precision float = .s (single precision float in FP register)
  Double precision float = .d (double float in even-odd FP register)
  Signed integer word = .w (signed integer in FP register)

## Slide 76: FP Compare and Branch Instructions
Instruction | Meaning | Format |  |  |  |  | 
c.eq.s fs, ft | cflag = ((fs) == (ft)) | 0x11 | 0 | ft5 | fs5 | 0 | 0x32
c.eq.d fs, ft | cflag = ((fs) == (ft)) | 0x11 | 1 | ft5 | fs5 | 0 | 0x32
c.lt.s fs, ft | cflag = ((fs) <= (ft)) | 0x11 | 0 | ft5 | fs5 | 0 | 0x3c
c.lt.d fs, ft | cflag = ((fs) <= (ft)) | 0x11 | 1 | ft5 | fs5 | 0 | 0x3c
c.le.s fs, ft | cflag = ((fs) <= (ft)) | 0x11 | 0 | ft5 | fs5 | 0 | 0x3e
c.le.d fs, ft | cflag = ((fs) <= (ft)) | 0x11 | 1 | ft5 | fs5 | 0 | 0x3e
bc1f Label | branch if (cflag == 0) | 0x11 | 8 | 0 | im16 |  | 
bc1t Label | branch if (cflag == 1) | 0x11 | 8 | 1 | im16 |  | 
FP unit (co-processor 1) has a condition flag
  Set to 0 (false) or 1 (true) by any comparison instruction
Three comparisons: equal, less than, less than or equal
Two branch instructions based on the condition flag

## Slide 77: Example 1: Area of a Circle
.data
pi: .double 3.1415926535897924
msg: .asciiz "Circle Area = "
.text
main:
ldc1 $f2, pi # $f2,3 = pi
li $v0, 7 # read double (radius)
syscall # $f0,1 = radius
mul.d $f12, $f0, $f0 # $f12,13 = radius*radius
mul.d $f12, $f2, $f12 # $f12,13 = area
la $a0, msg
li $v0, 4 # print string (msg)
syscall
li $v0, 3 # print double (area)
syscall # print $f12,13

## Slide 78: Example 2: Matrix Multiplication
void mm (int n, double x[n][n], y[n][n], z[n][n]) {
for (int i=0; i!=n; i=i+1)
for (int j=0; j!=n; j=j+1) {
double sum = 0.0;
for (int k=0; k!=n; k=k+1)
sum = sum + y[i][k] * z[k][j];
x[i][j] = sum;
}
}
Matrices x, y, and z are n×n double precision float
Matrix size is passed in $a0 = n
Array addresses are passed in $a1, $a2, and $a3
What is the MIPS assembly code for the procedure?

## Slide 79: Address Calculation for 2D Arrays
Row-Major Order: 2D arrays are stored as rows
Calculate Address of: X[i][j]
= Address of X + (i×n+j)×8 (8 bytes per element)
row 0
row i-1
row i
i × n
elements
n elements per row
j elements
X[i][j]
n elements per row
Address of Y[i][k] =
Address of Z[k][j] =
Address of Y + (i×n+k)×8
Address of Z + (k×n+j)×8

## Slide 80: Matrix Multiplication Procedure – 1/3
Initialize Loop Variables
mm: addu $t1, $0, $0 # $t1 = i = 0; for 1st loop
L1: addu $t2, $0, $0 # $t2 = j = 0; for 2nd loop
L2: addu $t3, $0, $0 # $t3 = k = 0; for 3rd loop
sub.d $f0, $f0, $f0 # $f0 = sum = 0.0
Calculate address of y[i][k] and load it into $f2,$f3
Skip i rows (i×n) and add k elements
L3: mul $t4, $t1, $a0 # $t4 = i*size(row) = i*n
addu $t4, $t4, $t3 # $t4 = i*n + k
sll $t4, $t4, 3 # $t4 =(i*n + k)*8
addu $t4, $a2, $t4 # $t4 = address of y[i][k]
l.d $f2, 0($t4) # $f2 = y[i][k]

## Slide 81: Matrix Multiplication Procedure – 2/3
Similarly, calculate address and load value of z[k][j]
Skip k rows (k×n) and add j elements
mul $t5, $t3, $a0 # $t5 = k*size(row) = k*n
addu $t5, $t5, $t2 # $t5 = k*n + j
sll $t5, $t5, 3 # $t5 =(k*n + j)*8
addu $t5, $a3, $t5 # $t5 = address of z[k][j]
l.d $f4, 0($t5) # $f4 = z[k][j]
Now, multiply y[i][k] by z[k][j] and add it to $f0
mul.d $f6, $f2, $f4 # $f6 = y[i][k]*z[k][j]
add.d $f0, $f0, $f6 # $f0 = sum
addiu $t3, $t3, 1 # k = k + 1
bne $t3, $a0, L3 # loop back if (k != n)

## Slide 82: Matrix Multiplication Procedure – 3/3
Calculate address of x[i][j] and store sum
mul $t6, $t1, $a0 # $t6 = i*size(row) = i*n
addu $t6, $t6, $t2 # $t6 = i*n + j
sll $t6, $t6, 3 # $t6 =(i*n + j)*8
addu $t6, $a1, $t6 # $t6 = address of x[i][j]
s.d $f0, 0($t6) # x[i][j] = sum
Repeat outer loops: L2 (for j = …) and L1 (for i = …)
addiu $t2, $t2, 1 # j = j + 1
bne $t2, $a0, L2 # loop L2 if (j != n)
addiu $t1, $t1, 1 # i = i + 1
bne $t1, $a0, L1 # loop L1 if (i != n)
Return:
jr $ra # return